## Slide 1: Building ML Controlled Instruments
Goals:
Develop a framework to unify automation of instruments
Avoid insular solutions with individual server-client interfaces
Flexible solution to be ready for advances in AI and ML tools

## Slide 2: Motivation and Advantages of pyTango
Proxy server:
  Coherent API for clients
  Asynchronous server
  Enables edge computing = Smart Proxy Server
  Dynamic device-database
  Model—context server (MCP) compatible to interface with large language model
  Compatible to Bluesky-Project (orchestration – system)
  Runs more than 10k devices at synchrotrons

## Slide 3: But: Many Manufacturers!
Image credit: Colin Ophus (LBNL), MRS Bulletin 2021
(a)
(b)
Instrument has detectors and cameras from multiple manufacturers
If you want to do anything useful, build APIs and orchestrators first!
U. Pratiush et al, Rev. Sci. Instr. 95 (2024).

## Slide 4: Asyncroscopy framework
LLM Agent
Model Context Protocol
Client
Electron Microscope
Instrument
Gatan Server
Ceos Corrector
AutoScript Mic.
AutoScript Stage
AutoScript Scan
Stage
EELS
Microscope
Scan
Aberration Corrector
Tiled Data Server
Local data
Separate data pipeline allows faster, asynchronous data streaming
All communication (arrows) via PyTango database
Vendor
agnostic
Notes: User, microscope
Each box is a different server
Communication through PyTango

## Slide 5: Digital Twins
LLM Agent
Model Context Protocol
Client
Electron Microscope
Instrument
DT EELS
DT Corrector
DT Microscope
DT Stage
DT Scan
Stage
EELS
Microscope
Scan
Aberration Corrector
Tiled Data Server
Local data
Separate data pipeline allows faster, asynchronous data streaming
All communication (arrows) via PyTango database
Model
Microscope
(abTEM)
Notes: Model + Synchronization
Two use cases:
Debugging code offline
Stable benchmark

## Slide 6: Starting the servers

## Slide 7: Cloudified Instruments at UTK
TEM/STEM Spectra 300, Thermo Fisher
SPM Jupiter, Oxford Instruments
SPM Cypher, Oxford Instruments
Nano Indenter, KLA
SPM/SEM FusionScope, QuantumDesign